## Slide 1: Intro to HW/SW Co-design
Yoav Etsion

## Slide 2: Admin
Welcome to the course 
Grading:
  Two home assignment (25%)
  Project: Analyze workload and propose potential HW acceleration
  Project is graded by:
    Implementation and final report (45%)
    Presentation (45%)
  Projects will be given in the last month of semester
  Presentations after MoedA period
Feel free to use whatever AI tools you want in the assignments and project
  But you are responsible to fully understand all AI products!

## Slide 3: Books
Classic books on HW/SW co-design focus on embedded systems
  Tune hardware for application
  Tune application for hardware
Not very relevant for this course
Some of the topics in the course are covered by Hennesey and Patterson, some by HW specs (e.g., PCIe, perf. counters), and many in recent literature
  We will try to properly cite the papers so you can read them

## Slide 4: The way we commonly see HW/SW boundary
We often split the computer system into SW and HW
We have “SW engineers” and “HW engineers”
CPU
OS
Application
SW
HW

## Slide 5: The way we commonly see HW/SW boundary
We often split the computer system into SW and HW
We have “SW engineers” and “HW engineers”
Very few engineers have good understanding of both HW and SW
Ignorance breeds a blame game 
CPU
OS
Application
SW
HW

## Slide 6: The way we commonly see HW/SW boundary
- “No hardware designer should be allowed to produce any piece of hardware until three software guys have signed off on it” - Prof. Andrew Tanenbaum (SW/OS person)
- “Computer theorists invent algorithms that solve important problems and analyze their asymptotic behavior (e.g. O(NlogN) or O(N3)). Computer architects set the constant factors for these algorithms…”
- Prof. Christos Kozyrakis (HW Architect)

## Slide 7: System view: Look at the big picture

## Slide 8: System view: Look at the big picture
Modern systems are humongous and complex
Typical events are handled by many servers, HW+SW
Different software layers (app, libs, OS, hypervisor)
Different hardware layers (CPU, GPU, memory)
Different networking layers (Ethernet, PCIe, DDRx, NVLink)

## Slide 9: The goal of this course: Look at the entire system
We hope to give you a good understanding of HW/SW interplay
We will examine some of the evolving requirements and constraints of both HW and SW
Understanding the entire system makes you better engineers
Knowledge breeds job security ;-)
CPU / GPU / NIC / Switch
OS
Application
SW
HW

## Slide 10: A different view of computer systems
Computers are built to solve problems
But all solutions have constraints
Both the problem and constraints are moving targets and are co-dependent
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 11: The rise of AI as a co-design example
AI is an example of how HW and SW helped shape the problem itself
Neural networks have been around for decades, but hardware could not support large nets
The ImageNet challenge triggered a change
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 12: ImageNet sets a challenge
In 2006 Prof. Fei-Fei Li of UIUC started curating a database of images to be used for research
  Inspired by Princeton’s WordNet
In 2010 the first ImageNet challenge was presented: classify images to a set of predefined classes
  e.g., cats, dogs, cars
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 13: CNNs found to be a good match for GPUs
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics
SVM on CPU
CNN on GPU
CNN on GPU
CNN on GPU
CNN on GPU
…
Error rate [%]

## Slide 14: The first AI accelerator: Google TPU
Google engineers realized that Tensors are a fundamental primitive for AI
In 2015 they introduced the Tensor Processing Unit
  aka, a matrix multiplier
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 15: The AI HW/SW co-design boom
After that, AI drove many HW efforts
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 16: But it started with evolving constraints
Moore’s Law and Dennard’s scaling
Moore’s Law: Transistor size “The number of transistors/mm2 doubles every 18mo.”
Dennard’s Scaling: Power density “The power of transistors/mm2 remains constant” (i.e., transistor power scales with Moore’s Law)
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 17: Dennard’s scaling
Dynamic power consumed by a digital circuit:
P = α*C*V2*f
Dennard projection:
  Voltage scales down
  Capacitance scales down (smaller devices)
  Frequency increases without consuming more power
It worked well, until it didn’t…
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 18: Dennard, Moore, and performance
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 19: Dennard, Moore, and performance
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 20: CPUs are limited
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 21: Data growth is killing us
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 22: Are accelerators always the answer?
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics
No (even if we ignore the high manufacturing costs)
The complexity of HW designs is getting out of hand, and the broken VLSI tool flow cannot cope
Kernighan's Law on software: “Debugging is twice as hard as writing the code in the first place. Therefore, if you write the code as cleverly as possible, you are, by definition, not smart enough to debug it.”
Especially if the tool flow is broken

## Slide 23: The broken VLSI tool flow: Verification
Hardware complexity is limited by our verification tools
Formal verification is limited
    Hard to generate formal specification
    Computation explodes very fast, especially if there’s state (SAT is NP-complete)
  Functional verification still rules
    Coverage is the major limitation of functional verification
  Result: We need 2-4 verification engineers for each designer
  Engineering cost is the major expense of HW design
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 24: The broken VLSI tool flow: Verification
How can we scale hardware verification to manage more complex designs?
    Open question…
    GenAI for coverage?
    GenAI for formal spec (active research field)
We tend to try GenAI when we run out of algorithmic ideas…
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 25: The broken VLSI tool flow: The full flow
Architect writes arch. Specification doc.
Verification engineer needs to understand both
Designer codes RTL
SW writes func+timing simulators
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 26: The broken VLSI tool flow: The full flow
Architect writes arch. Specification doc.
Designer codes RTL
Verification engineer needs to understand both
RTL SW simulator (~1000 cy/s)
Emulator (limited, ~100k cy/s)
External IP (gate-level)
IP model for simulator
IP model for emulator
SW writes func+timing simulators

## Slide 27: The broken VLSI tool flow: The full flow
Architect writes arch. Specification doc.
Designer codes RTL
Verification engineer needs to understand both
RTL SW simulator (~1000 cy/s)
Emulator (limited, ~100k cy/s)
External IP (gate-level)
IP model for simulator
IP model for emulator
SW writes func+timing simulators

## Slide 28: Some inalienable truths
RTFM
PEBKAC
Problem Exists Between Keyboard And Chair

## Slide 29: The broken VLSI tool flow: Humans…
Architecture documents have bugs
Designs are manually coded and are therefore buggy
Simulators are manually coded and are therefore buggy
IP models are manually coded from IP spec. and are buggy
  We found bugs in functionality, timing
RTL simulator/emulator too slow for complex test case
SW simulators are decoupled from RTL implementation
  Limited use for functional/performance verification
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 30: The broken VLSI tool flow: RTL
The register transfer language (RTL) abstraction is too low level
  Forces designers to focus on mapping functionality to registers and wires, not getting the functionality right
    >80% of code is just connecting wires
    Verilog, SystemVerilog, Chiesel, PyRTL, …
Akin to writing MS Office in assembly language
New High-level synthesis languages are no match either
    Use incompatible SW constructs (e.g., arrays, loops) so abstractions are not consistent across transformations
    E.g., Xilinx/AMD Vivado, Cadence Stratus, Synopsys Symphony
  End result: Existing VLSI tool flow restricts HW complexity
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 31: Processing in-/near-storage: When the solution to the gap is unclear
Axiom 1: Most of the data resides in storage
Axiom 2: Moving data to the processor is expensive
Obvious solution: Let’s move the computation inside or near storage
But it turns out to be not so obvious
Problem
Algorithm
Software
Hardware/Arch.
VLSI flow
Devices
Physics

## Slide 32: Is processing in/near storage going really feasible?
Data is aggressively compressed
  DB tables: type-specific encoding + compression
  Images: JPEG, PNG (LZ), …
  Video: H265, …
Any processing must decompress data before processing, then compress again
  At high bandwidth
In-storage: (de)compress inside memory array?
Near storage: must keep controller dirt-chip
In server: OS operation (e.g., dedup), custom DBs

## Slide 33: Looking at the entire system
We need to see the bigger picture
Learn about evolving HW and SW trends
Learn about evolving HW and SW constraints
Understand how the entire system works

## Slide 34: Tentative outline
 | Topic
1 | Principles of performance evaluation: Throughput, latency, arrival rate, service time, Little’s Law
2 | Hardware performance counters: (guest speaker: Anton Hanna, Intel) Usage, hierarchical performance analysis
3 | Identifying bottlenecks: Call graph, flame graph common suspects: memory, network, storage
4 | Accelerator patterns and design concepts: Systolic arrays (Google TPU), static/dynamic dataflow in CGRA (Speedata APU)
5 | Hardware design concepts: PCIe interconnect, architecture, interfaces, performance, PCIe-based accelerators

## Slide 35: Tentative outline
 | Topic
6 | Cloud workload challenges: Virtual machines, containers, HW offload
7 | Cloud workload challenges: Virtual memory, 2D page walk, performance impact, HW offload proposals
8 | Cloud workload challenges: Advanced virtual memory, TLBs, TLB shootdown
9 | Cloud workload challenges: Microservices, Lambda/Function programming, HW/SW disparity
10 | DRAM: How it works, performance and power limitations, security issues (RowHammer)

## Slide 36: Thank you Questions?