## Slide 1: Accelerator Design Patterns
Yoav Etsion

## Slide 2: How do accelerators work?
We’ve found a point where software needs dedicated hardware
We’ve managed to make a case for dedicated hardware
  Very expensive
How do we design an accelerator?
  Software interface and stack
  Hardware
Two case studies:
  Google TPU (Tensor Processing Unit)
  Speedata APU (Analytics Processing Unit)

## Slide 3: HW/SW interface for accelerators
Rule 1: Do not expect end users to change their code
  Customers have a large code base
  Huge effort (cost) to change existing code base
Rule 2: If SW must change, confine changes in runtime/libraries
  May only require users only to compile their code
  In some cases, not even that
Rule 3: Don’t break user’s code
  If HW does not support an operation, run it on the CPU
  Reduced performance/power improvement is better than broken user code

## Slide 4: HW design patterns
Many recent accelerators use one of two HW patterns
Systolic array
  E.g., Google, Habana
Dataflow primitives
  Often times as coarse/grain reconfigurable arrays (CGRAs)
  E.g., Speedata, SambaNova, NextSilicon

## Slide 5: Systolic arrays
Proposed by Kung and Leiserson in 1979
  Extensively studies in the 1980s
  H. T. Kung, C. E. Leiserson: Algorithms for VLSI processor arrays; in: Introduction to VLSI Systems; Addison-Wesley, 1979
Circuit inputs are processed on each cycle
No control circuitry
Most efficient silicon utilization
Adder

## Slide 6: Systolic arrays
Circuit inputs are processed on each cycle
No control circuitry
Most efficient silicon utilization
Adder
Cycle 1
(start)
(end)

## Slide 7: Systolic arrays
Circuit inputs are processed on each cycle
No control circuitry
Most efficient silicon utilization
Where’s the problem?
Adder
Cycle 2
(start)
(end)

## Slide 8: Systolic arrays
The problem arises if an input is not ready
There’s no control circuit, so an output will be generated
In other word: “garbage in, garbage out”
Adder
Cycle 1

## Slide 9: Dataflow
The dataflow model was originally proposed by Karp and Miller as a parallel execution model in 1966
  R. Karp and R. Miller. “Properties of a Model for Parallel Computations: Determinacy, Termination, Queueing”. SIAM J. Appl. Math. 14, 6 (Nov 1966).
In short :
  Data is passed as tokens, and we can check if a token is available
  Execute the operation when the input data is ready
How do we do it at the circuit level?

## Slide 10: Static vs. dynamic dataflow
The dataflow model triggers an event only when all of its inputs are ready
Adder
What’s the fundamental difference from systolic arrays?

## Slide 11: Static vs. dynamic dataflow
The dataflow model triggers an event only when all of its input tokens are ready
Static dataflow: If there are multiple sets of input tokens, they are executed in-order
Adder

## Slide 12: Static vs. dynamic dataflow
The dataflow model triggers an event only when all of its input tokens are ready
Static dataflow: If there are multiple sets of input tokens, they are executed sequentially
Dynamic dataflow: Execute whenever set of matching input tokens that is available (does that remind you of something?)
Adder

## Slide 13: Dataflow circuits
At the circuit-level, add data/ready signals to all interfaces
Operator process (consumes) inputs only when valid and consumer is ready
We can define a set of primitives from which we built circuits
  Primitives require additional circuitry
Example by Josipovic et al.
  L. Josipović, A. Guerrieri and P. Ienne, "From C/C++ Code to High-Performance Dataflow Circuits“. In IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems 41(7), July 2022

## Slide 14: Dataflow limitations
What happens when we have a loop in the circuit?
  E.g., register bypass in the pipeline
If EX stage needs input from MEM, first token will never be valid
Solution: Inject NULL token
  Oron Port, "DFiant: A Dataflow Hardware Description Language ". Phd Thesis, Technion 2021.
Fetch
Decode
Execute
Memory
Writeback

## Slide 15: Case Study: TPU

## Slide 16: Google TPU
In 2013 Google projected that if users use 3 minute of DNN-based voice search per day, they will need to double their data centers’ computational capacity
Started working on a hardware accelerator for NN inference
  Identified that matrix multiplication is the main bottleneck
  Went back to 1980s literature on systolic arrays
Deployed in 2015, published in 2017
  Joupi et al., “In-Datacenter Performance Analysis of a Tensor Processing Unit”. In ISCA 2017
Recently announced the 7th generation TPU

## Slide 17: Why matrix multiplication?
NNs are composed of layers of “synapses”
The inputs to each synapse are the outputs of the previous layer multiplied by a weight vector
dot_product(weights, inputs)
Synapse takes sum and applies normalization function

## Slide 18: Why matrix multiplication?
In other words:
X
Inputs
Weights

## Slide 19: TPU’s systolic array
256x256 array of 8-bit integer MACs
  Product is 16b
64k ops/cycle for 8-bit ints
  Can operate at slower rate on larger formats
Reads/writes 256 values/cycles
Weights preloaded to array, and then inputs are streamed

## Slide 20
https://telesens.co/2018/07/30/systolic-architectures/
Inputs are staggered since systolic array has no control

## Slide 21
https://telesens.co/2018/07/30/systolic-architectures/

## Slide 22
https://telesens.co/2018/07/30/systolic-architectures/

## Slide 23
https://telesens.co/2018/07/30/systolic-architectures/

## Slide 24
https://telesens.co/2018/07/30/systolic-architectures/

## Slide 25
https://telesens.co/2018/07/30/systolic-architectures/

## Slide 26
https://telesens.co/2018/07/30/systolic-architectures/

## Slide 27
https://telesens.co/2018/07/30/systolic-architectures/

## Slide 28: TPU’s systolic array limitation
A systolic array is timed only by the clock, no control
Q: What happens when the input data is not ready
A: Need to preload inputs into an on-chip staging buffer
Q: What about sparse matrices?
A: Still a major challenge; Unknown how addressed in TPUvX

## Slide 29: TPU block diagram
Joupi et al., In-Datacenter Performance Analysis of a Tensor Processing Unit , ISCA 2017

## Slide 30: TPU gen1
PCIe gen3
32GB DRAM
384W
<331mm2
  *less than ½ of Haswell
Joupi et al., In-Datacenter Performance Analysis of a Tensor Processing Unit , ISCA 2017

## Slide 31: TPU: Area distribution
Joupi et al., In-Datacenter Performance Analysis of a Tensor Processing Unit , ISCA 2017

## Slide 32: TPU: Power benefits

## Slide 33: TPU: Design space exploration
Examine how scaling different parameters affect performance
Memory = memory bw
Clock+ = freq. & accums
Clock = only freq.
Matrix+ = sys. array& accums
Matrix = sys. array
Perf/TPU

## Slide 34: TPU: HW/SW interface
Philosophy: TPU should behave like an external FPU
Provide ~12 commands the host can trigger
Examples listed in the paper:
  Read_Host_Memory: Read data from the CPU to the unified SRAM buffer
  Read_Weights: Read weights into array input FIFOs
  MatrixMultiply: Trigger matrix multiplication on N inputs
  Activate: apply normalization to data in accumulator memory and write to unified buffer
  Write_Host_Memory: Write data from unified buffer to CPU memory

## Slide 35: TPU: HW/SW interface
User-space driver controls the TPU
  Reformats data
  Executes TPU instructions
Use blocked matrix multiplication to split large matrices
  Not clear if it is done in driver or higher up the stack (e.g., PyTorch, Tensorflow)
Users need not change their code!
  Code written in high-level frameworks, e.g., PyTorch, Tensorflow

## Slide 36: Scaling out newer generations: TPUv3
4 chips per board
Liquid cooling

## Slide 37: Scaling out newer generations: TPUv3
A TPU pod
3D torus network
Not clear how many sockets in a pod

## Slide 38: Scaling out newer generations: TPUv5
256 chips per pod
  (I suspect ¼ - ½ of what we see in the image)
3D torus network

## Slide 39: Case Study: APU

## Slide 40: APU
Started as academic research on CGRAs in 2012
Motivation was to build a reconfigurable architecture for CUDA
  Use spatial computing instead of GPU’s von Neumann core
  Move data directly between functional units instead of register file
First paper published in 2014
  Voitsechov and Etsion. “Single-graph multiple flows: energy efficient design alternative for GPGPUs”. In ISCA 2014
Speedata founded in late 2019

## Slide 41: A dataflow CGRA
2D grid of functional units
  E.g., LSU, ALU, FPU, special function units
Units are connected by a configurable network
Reconfigurable design allows mapping the computation onto the grid
ALU
ALU
LD/S
ALU
ALU
FPU
ALU
SFU
ALU
FPU
SFU
ALU
FPU
ALU
ALU
SFU
FPU
ALU
ALU
LD/S
ALU
SFU
FPU
ALU
SFU
ALU
FPU
ALU
ALU
ALU
FPU
ALU
ALU
ALU
FPU
ALU

## Slide 42: A dataflow CGRA
CGRAs have been proposed in the past, e.g,:
  TRIPS in 2003
    Sankaralingam et al., "Exploiting ILP, TLP, and DLP with the polymorphous TRIPS architecture“. In ISCA 2003.
  Tartan in 2006
    Mishra et al., “Tartan: evaluating spatial computation for whole program execution”. In ASPLOS 2006
  DySER in 2011
    Govindaraju et al., “Dynamically Specialized Datapaths for energy efficient computing”. In HPCA 2011.
All targeted single-threaded workloads
Our take: Massively data parallel code - CUDA
ALU
ALU
LD/S
ALU
ALU
FPU
ALU
SFU
ALU
FPU
SFU
ALU
FPU
ALU
ALU
SFU
FPU
ALU
ALU
LD/S
ALU
SFU
FPU
ALU
SFU
ALU
FPU
ALU
ALU
ALU
FPU
ALU
ALU
ALU
FPU
ALU

## Slide 43: Programming the CGRA: CUDA-like parallelism
❶ Kernel/Task
❷
Compiler transforms kernel code to dataflow graph(s)
❸ Map:
Compiler maps dataflow graph to CGRA and conf. network
Reconfigurable fabric
❹ Stream entire dataset through the configured fabric

## Slide 44: Branches
Sequential code is broken into basic blocks
Basic block: A sequence of instructions executed between branches
Different thread may have different branch outcomes
Result: Branch-divergent code

## Slide 45: Branches: GPU
GPUs bind threads into groups (warps)
All threads in a group (warps) need to execute both ‘then’ and ‘else’ clauses
  Unneeded clause is executed as nops
Breaking groups dynamically is inefficient
Result: GPUs are highly inefficient for branch-divergent code

## Slide 46: Branches: APU
Each basic block is a dataflow graph
APU runs one dataflow graph at a time
Threads and graphs are scheduled so cycles are not wasted on nops
  Reconfiguration is very fast (10s of cycles)
Result: APU is very efficient even in branch-divergent code
  Voitsechov and Etsion. “Control flow coalescing on a hybrid dataflow/von Neumann GPGPU”. In MICRO 2015.

## Slide 47: The dataflow memory challenge
A compiler takes your code and converts it into a directed graph
Nodes are functional units
Edges are registers
What about dependencies in memory?
  That’s the biggest challenge in dataflow computing

## Slide 48: The dataflow memory challenge
Memory system allows keeping multiple accesses in-flight
  Known as memory-level parallelism (MLP)
Data returned from memory in some order
  Cache/memory units need to reorder returned data and stream it into the grid
  Dynamic dataflow
Inside the grid, all dependencies and latencies are known
  Static dataflow

## Slide 49: Speedata: What is data analytics and why go there?
Data is collected from many sources and ingested into storage
  Sources include sensors, browsers, code agents
Data itself can be
  structured (e.g., relational tables)
  semi-structured (e,.g., nested relational tables)
  unstructured (e.g., text, images)
Analyzed using relational operations (e.g., SQL, dataframes)
[credit for copyrighted images goes to respective companies]
Social networks
Adtech
Manufacturing
Pharma

## Slide 50: Mapping SQL to multiple CGRAs in the APU Filter + JOIN + GROUPBY by example
1.6Tbps
Decompress
Decode
Process
Decompress
Decode
Process
Decompress
Decode
Process
Record
Field manipulation
Example: SUM(IF(name= ‘Tom’ OR name=‘Scott’))
Filter records
ALU
ALU
LD/S
ALU
ALU
FPU
ALU
SFU
ALU
FPU
SFU
ALU
FPU
ALU
ALU
SFU
FPU
ALU
ALU
LD/S
ALU
SFU
FPU
ALU
SFU
ALU
FPU
ALU
ALU
ALU
FPU
ALU
ALU
ALU
FPU
ALU
ALU
ALU
LD/S
ALU
ALU
FPU
ALU
SFU
ALU
FPU
SFU
ALU
FPU
ALU
ALU
SFU
FPU
ALU
ALU
LD/S
ALU
SFU
FPU
ALU
SFU
ALU
FPU
ALU
ALU
ALU
FPU
ALU
ALU
ALU
FPU
ALU
Record
Encode
Encode
Encode
Compress
Compress
Compress
Data flow
On-chip NoC + memory banks
JOIN
GROUPBY
Notes: Minimize number of trips to memory

## Slide 51: APU: HW/SW interface
We do not expose the interface, but it is hidden from the users
End users write SQL or dataframe queries
We plug into existing analytics framework to offload computation into the APU
Users need not change their code!

## Slide 52: Integration with software ecosystem
Parser
SQL Query
Dataframes
Pandas
Logical Plan
Physical Plan
X86/JVM Code Generator
APU Code Generation
Scheduler
bin
bin
Worker-1
Worker-2
Worker-3
Worker-4
Worker-N
Plugin
Speedata query compiler
Coordinator Node Software
SPEEDATA
SPEEDATA
Operators that are not supported yet are redirected to x86
  Rule #3…

## Slide 53: Summary
A key challenge in HW/SW co-design: Don’t break user code!
Dominant accelerator design paradigms:
  Systolic arrays (for matrix multiplication)
  Coarse-grain reconfigurable arrays (CGRA)
    And the general dataflow model
Two case studies:
  Google TPU: Catapulted Google’s AI efforts
  Speedata APU: Commercial CGRA for data analytics

## Slide 54: Thank you Questions?