## Slide 1: PCIe (Peripheral Component Interconnect Express)
Yoav Etsion

## Slide 2: Welcome to the PCIe spec 
We’ll only cover the highlights…

## Slide 3: PCIe overview
PCIe connects CPUs to all devices in the system
  Except for DRAM
  Descendant of ISA, PCI, PCI-X, AGP

## Slide 5: PCIe overview
PCIe connects CPUs to all devices in the system
  Except for DRAM
  Descendant of ISA, PCI, PCI-X, AGP
Modern servers are shipping with PCIe gen5/gen6 slots
  Gen7 spec has been released
Tree topology*
  Ignoring rarely used NTB and MR-IOV features
Guaranteed packet delivery (ack on each packet; no packet loss)
Devices can have multiple functions (e.g., NIC with two ports)

## Slide 6: PCIe topology
CPU
PCIe Root Complex
Device
PCIe Endpoint
Memory

## Slide 7: PCIe topology
CPU
PCIe Root Complex
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
Memory

## Slide 8: PCIe topology
CPU
PCIe Root Complex
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Switch
Memory

## Slide 9: PCIe topology in the spec
Bridge devices connect other protocols - e.g., PCI-X, USB

## Slide 10: PCIe topology
CPU
PCIe Root Complex
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Switch
Memory
PCIe link

## Slide 11: PCIe topology
CPU
PCIe Root Complex
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Switch
Memory
Bus
Bus

## Slide 12: PCIe enumeration
At boot time, the root complex enumerates the network
  Checks endpoint configuration space
  Read device vendor, type, class
  Assigns configuration parameters to each endpoint
  Negotiates speed with each device
  Assigns bus numbers
Typically executed by the BIOS, and device map passed to the OS
  OS can also redo the enumeration if BIOS allows

## Slide 13: PCIe topology after enumeration
CPU
PCIe Root Complex
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Switch
Memory
Bus 0x1
Bus 0x2
0x1
0x2
0x3
0x1
0x2
0x3

## Slide 14: PCIe addressing: Bus:Device.Function (BDF)
CPU
PCIe Root Complex
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Switch
Memory
Bus 0x1
Bus 0x2
0x1
0x2
0x3
0x1
0x2
0x3
The device address is the ~path from the root to the device
Known as BDF
0
1
BDF=2:2.1
BDF=1:2.0

## Slide 15: Addressing examples

## Slide 16: Device configuration space
Devices export their parameters through a configuration space

## Slide 17: Device configuration space
Devices export their parameters through a configuration space

## Slide 18: Device configuration space
Devices export their parameters through a configuration space
The root complex negotiates some parameters with devices

## Slide 19: PCIe topology with multiple CPUs
CPU
PCIe Root Complex
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Switch
Memory
CPU
PCIe Root Complex
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Switch
Memory
Vendor-specific link (Intel QPI, AMD HyperTransport)

## Slide 20: PCIe topology with multiple CPUs
Device-to-device can be limited by topology
Example:
  We want direct GPU-NIC connectivity
  What happens if we place them randomly?

## Slide 21: PCIe topology with multiple CPUs Bad placement
CPU
PCIe Root Complex
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Switch
Memory
CPU
PCIe Root Complex
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Switch
Memory
Vendor-specific link (Intel QPI, AMD HyperTransport)
GPU
NIC

## Slide 22: PCIe topology with multiple CPUs Good placement
CPU
PCIe Root Complex
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Switch
Memory
CPU
PCIe Root Complex
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Endpoint
PCIe Switch
Memory
Vendor-specific link (Intel QPI, AMD HyperTransport)
GPU
NIC

## Slide 23: PCIe lanes

## Slide 24: PCIe lanes
PCIe links are composed of serial lanes
  E.g., a x16 device supports a link with 16 lanes
Each lane is full duplex
PCIe uses Low-voltage differential signaling (LVDS)
  Passing a bit over two wires: D+ and D-
  Receiving end checks V=D+-D-
  Why?
Total 4 wires per lane (two wires in each direction)

## Slide 25: PCIe LVDS signaling

## Slide 26: PCIe lane speeds
Generation | Lane speed (TPS) | Lane speed (bits/bytes) | 
PCIe 1.0 | 2.5GT/s | 2gbs = 250MB/s | 
PCIe 2.0 | 5.0GT/s | 4gbs = 500MB/s | 
PCIe 3.0 | 8.0GT/s | 8gbs = 1GB/s | 
PCIe 4.0 | 16.0GT/s | 16gbs = 2GB/s | 
PCIe 5.0 | 32.0GT/s | 32gbs = 4GB/s | 
PCIe 6.0 | 64.0GT/s | 64gbs = 8BG/s | PAM4 signaling

## Slide 27: PCIe HW/SW interface: Host-to-Device
Device define memory spaces that can be mapped to OS/application
Device’s control registers and memory (as defined by their designer) are mapped to these regions
Regions controlled by Base Address Registers (BARs) in config space
  Up to 6 BARs in 32b mode, 3 BARs in 64b mode

## Slide 28: PCIe HW/SW interface: Host-to-Device
Broadcom NIC defined 3x 64KB spaces

## Slide 29: PCIe HW/SW interface: Host-to-Device
Broadcom NIC defined 3x 64KB spaces
BIOS/OS maps BARs to physical address space at enumeration time
Phys. Address space (64b)
Phys. Memory
0x91b30000
BAR0
BAR2
BAR4
0x91b40000
0x91b50000
config

## Slide 30: PCIe HW/SW interface: Host-to-Device
Host only accesses device logic through BARs
  And whatever the designer put in the BARs
When host accesses a BAR, the PCIe root complex translates the memory address into a BDF address
Packet is sent to BDF address

## Slide 31: PCIe HW/SW interface: Device-to-Host
Devices see the IO address space, defined by the host
All device accesses go to addresses in the IO space
  Even interrupts use special addresses
Host uses IOMMU to map device memory accesses to phys. memory
IOMMU uses device’s BDF address to find the per-device page table

## Slide 32: PCIe HW/SW interface: Device-to-Host

## Slide 33: PCIe support for device virtualization HW/SW co-design example
A device can be mapped to a VM/container/app using the IOMMU
  But the number of devices is limited
  Can we dynamically allocate new virtual devices?
PCIe Single-root IO Virtualization (SR-IOV)
  Every device has a physical function 0
  SR-IOV lets host dynamically create/destroy virtual functions
    Using Hypervisor-controlled physical function 0
  Each virtual function has its own BARs that can be mapped to VM/container/app
Device designer defines how to multiplex requests from all its functions

## Slide 34
Native system

## Slide 35
=hypervisor
=VMs
SW virtualization (no SR-IOV)

## Slide 36
=hypervisor
=VMs
SR-PCIM: SW that controls SR-IOV
(single-root PCI manager)
Translation agent: Address translation logic in IOMMU
ATPT: IOMMU page table
ATC: Address translation cache
(more on that soon)
HW virtualization (SR-IOV)
Chip boundary

## Slide 37: HW/SW co-design challenges in PCIe
PCIe is a central component in modern systems
As such, it poses many improvement opportunities
  E.g., performance bottlenecks, security challenges, scaling challenges
Let’s examine some of the challenges in the virtualization domain

## Slide 38: IOMMU throughput: The challenge
All traffic to the host goes through the IOMMU
IOMMU translation throughput can become a bottleneck
  800gbs Ethernet NIC = 100GB/s
  1500B frames: 66,666,667 translations/sec
  64B frames: 1,562,500,000 translations/sec

## Slide 39: IOMMU throughput
Hot research topic
Malka et al., “rIOMMU: Efficient IOMMU for I/O devices that employ ring buffers”. In ASPLOS 2015
  Idea: Refactor IOMMU to use lists of buffers instead of page tables
  Pros: Access pattern matches NIC traffic
  Cons: GPUs exhibit different traffic patterns (not just ring buffers)
Real world (PCIe specification):
  Multiple IOMMUs per chip/root complex
  Increase IOTLB as much as possible
  Distribute IOTLB by pushing caches to devices

## Slide 40
=hypervisor
=VMs
SR-PCIM: SW that controls SR-IOV
(single-root PCI manager)
Translation agent: Address translation logic in IOMMU
ATPT: IOMMU page table
ATC: Address translation cache
(now’s the time!)
- Aka DeviceTLB
HW virtualization (SR-IOV)

## Slide 41: IOMMU throughput: Distributed caching
Base idea: Devices know which buffers they are going to access
  Let devices cache translations internally
IOMMU offers address translation service (ATS)
Devices can ask IOMMU for VA->PA translation when needed
Store translation in the devices address translation cache (ATC)
Send requests to host using phys. addresses
Pros:
  Requests with phys. addresses do not require translation
  Reduces load from IOMMU translation logic
Cons: Well…

## Slide 42: Malicious devices: The challenge
Allowing devices to use PAs creates a security vulnerability
  Can we trust a device to only access PA returned by PCIe’s ATS?
Vulnerability demonstrated using Thunderbolt devices
Markettos et al. “Thunderclap: Exploring vulnerabilities in operating system IOMMU protection via DMA from untrustworthy peripherals”. In NDSS 2019
  Idea: Thunderbolt tunnels PCIe packets over USB-C
  Attack: Implement a malicious NIC that uses ATS on a Thunderbolt FPGA card
  Mitigation: Block ATS for USB controllers (at performance cost)

## Slide 43: Malicious devices: Defenses?
Open research area
Alam et al., "CryptoMMU: Enabling Scalable and Secure Access Control of Third-Party Accelerators”. In MICRO 2023
  Idea: Cryptographically sign ATS translation; allows only signed translations through IOMMU
  Pros: simple hardware; nice solution
  Cons: Not fully compatible with existing devices
More ideas are welcome

## Slide 44: PCIe: Summary
PCIe is a crucial component in modern system
  New CXL standard builds on PCIe
Built to serve devices inside a single server
  Several companies that tried to scale it beyond the server failed
High-performance interconnect that binds all devices together
Very effective, but presents many challenges, e.g.,
  Performance, esp. IOMMU
  Secure system from malicious/buggy devices
  And we haven’t even discussed device-to-device communications