## Slide 1: Virtual Memory
Yoav Etsion

## Slide 2: Virtual memory recap
Virtual memory is a great abstraction for decoupling program view of memory from the physical view
  Simplified isolation between applications
  Allows OS to manage physical memory without affecting program correctness
  Provides programmers with an abstract view of memory
Virtual memory translation has become terrible for performance
  Translation times, esp. in virtual systems, are a major run time overhead
  Hardware countermeasures impose area and power overheads
  Size of caches (100 MBs) and physical memory (TBs) is increasing

## Slide 3: Virtual memory recap
Radix tree page tables on x86_64 for 4KB pages
sign ext.
0
29
DIR
TABLE
OFFSET
Linear Address Space (4K Page)
11
20
512 entry Page Table
512 entry
Page Directory
PDE
4KByte Frame
data
9
9
12
PTE
CR3 (PDPTR)
40 (4KB aligned)
28
28
12
21
30
38
512 entry Page Directory
Pointer Table
PDP entry
28
9
PDP
PML4
39
47
63
512 entry PML4 Table
PML4 entry
9
28

## Slide 4: Virtual memory recap
Radix tree page tables on x86_64 for 2MB pages
sign ext.
0
29
DIR
OFFSET
Linear Address Space (2M Page)
20
512 entry
Page Directory
PDE
2MByte Frame
data
9
21
CR3 (PDPTR)
40 (4KB aligned)
19
21
30
38
512 entry Page Directory
Pointer Table
PDP entry
28
9
PDP
PML4
39
47
63
512 entry PML4 Table
PML4 entry
9
28

## Slide 5: Virtual memory recap
Page tables reside in memory
  Each translation requires multiple memory accesses
    Typically, more than once
  Might be required for each load/store!
Translation lookaside buffer (TLB)
  Hardware cache for recently used PTEs (locality)
  Speeds up translation
  Fewer than 100 entries
    Modern CPUs have L2 TLB as well
  2 to 8 way associative
  TLB access time is faster than L1 cache access time
Yes
No
TLB Hit ?
Access
Page Table
Virtual Address
Physical
Addresses
TLB Access

## Slide 6: TLBs: Single core
Thread accesses VA1
CPU1
TLB
L1
L2
LLC

## Slide 7: TLBs: Single core
Thread accesses VA1
TLB caches mapping
CPU1
TLB
L1
L2
LLC
VA1->PA1

## Slide 8: TLBs: Single core
Thread accesses VA1
TLB caches mapping
Thread frees memory
  munmap, not just free
CPU1
TLB
L1
L2
LLC
VA1->PA1

## Slide 9: TLBs: Single core
Thread accesses VA1
TLB caches mapping
Thread frees memory
  munmap, not just free
OS flushes mapping from TLB
CPU1
TLB
L1
L2
LLC
VA1->PA1

## Slide 10: TLBs: Single core
Thread accesses VA1
TLB caches mapping
Thread frees memory
  munmap, not just free
OS flushes mapping from TLB
CPU1
TLB
L1
L2
LLC

## Slide 11: TLBs: Single core
Thread accesses VA1
TLB caches mapping
Thread frees memory
  munmap, not just free
OS flushes mapping from TLB
All is well 
CPU1
TLB
L1
L2
LLC

## Slide 12: TLBs: Multicore
Thread1 accesses VA1
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1

## Slide 13: TLBs: Multicore
Thread1 accesses VA1
Thread2 accesses VA1 on a different core
  Different or migrated thread
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1
VA1->PA1

## Slide 14: TLBs: Multicore
Thread1 accesses VA1
Thread2 accesses VA1 on a different core
  Different or migrated thread
Thread1 unmaps memory
  Using munmap, not just free (free returns buffer to malloc poll)
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1
VA1->PA1

## Slide 15: TLBs: Multicore
Thread1 accesses VA1
Thread2 accesses VA1 on a different core
  Different or migrated thread
Thread1 unmaps memory
  Using munmap, not just free (free returns buffer to malloc poll)
OS flushes mapping from TLB
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1
VA1->PA1

## Slide 16: TLBs: Multicore
Thread1 accesses VA1
Thread2 accesses VA1 on a different core
  Different or migrated thread
Thread1 unmaps memory
  Using munmap, not just free (free returns buffer to malloc poll)
OS flushes mapping from TLB
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1

## Slide 17: TLBs: Multicore
Thread1 accesses VA1
Thread2 accesses VA1 on a different core
  Different or migrated thread
Thread1 unmaps memory
  Using munmap, not just free (free returns buffer to malloc poll)
OS flushes mapping from TLB
See the problem?
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1

## Slide 18: TLBs: Multicore
Thread accesses VA1
Thread accesses VA1 a different core
  Different or migrated thread
Thread frees memory
  munmap, not just free
OS flushes mapping from TLB
See the problem?
A TLB holds a stale mapping
  Correctness & security issue
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1

## Slide 19: The TLB coherence problem
Hardware does not enforce coherence across TLBs
  Although research showed the benefits
  E.g.,
    Romanescu et al., "UNified Instruction/Translation/Data (UNITD) coherence: One protocol to rule them all“. In HPCA 2010
    Villavieja et al., "DiDi: Mitigating the Performance Impact of TLB Shootdowns Using a Shared TLB Directory“. In PACT 2011

## Slide 20: The TLB coherence problem
Hardware does not enforce coherence across TLBs
  Although research showed the benefits
  E.g.,
    Romanescu et al., "UNified Instruction/Translation/Data (UNITD) coherence: One protocol to rule them all“. In HPCA 2010
    Villavieja et al., "DiDi: Mitigating the Performance Impact of TLB Shootdowns Using a Shared TLB Directory“. In PACT 2011
But OS frequently needs to unmap pages and change translations
  Free memory, move pages, change page permissions, swapping, etc.

## Slide 21: The TLB coherence problem
Hardware does not enforce coherence across TLBs
  Although research showed the benefits
  E.g.,
    Romanescu et al., "UNified Instruction/Translation/Data (UNITD) coherence: One protocol to rule them all“. In HPCA 2010
    Villavieja et al., "DiDi: Mitigating the Performance Impact of TLB Shootdowns Using a Shared TLB Directory“. In PACT 2011
But OS frequently needs to unmap pages and change translations
  Free memory, move pages, change page permissions, swapping, etc.
How do we make TLBs coherent using today’s hardware?

## Slide 22: TLB shootdown

## Slide 23: TLB shootdown
Thread1 frees memory
  munmap, not just free
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1
VA1->PA1

## Slide 24: TLB shootdown
Thread1 frees memory
  munmap, not just free
OS on CPU1:
  Locks entry in page table
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1
VA1->PA1
Page Table

## Slide 25: TLB shootdown
Thread1 frees memory
  munmap, not just free
OS on CPU1:
  Locks entry in page table
  Sends inter-processor interrupt (IPI) to other CPUs
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1
VA1->PA1
Page Table

## Slide 26: TLB shootdown
Thread1 frees memory
  munmap, not just free
OS on CPU1:
  Locks entry in page table
  Sends inter-processor interrupt (IPI) to other CPUs
  (Other CPUs invoke SW handler and flush mapping from TLB)
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1
VA1->PA1
Page Table

## Slide 27: TLB shootdown
Thread1 frees memory
  munmap, not just free
OS on CPU1:
  Locks entry in page table
  Sends inter-processor interrupt (IPI) to other CPUs
  (Other CPUs invoke SW handler and flush mapping from TLB)
  (Other CPUs ack CPU1)
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1
Page Table

## Slide 28: TLB shootdown
Thread1 frees memory
  munmap, not just free
OS on CPU1:
  Locks entry in page table
  Sends inter-processor interrupt (IPI) to other CPUs
  (Other CPUs invoke SW handler and flush mapping from TLB)
  (Other CPUs ack CPU1)
  Flushes mapping in CPU1
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1
Page Table

## Slide 29: TLB shootdown
Thread1 frees memory
  munmap, not just free
OS on CPU1:
  Locks entry in page table
  Sends inter-processor interrupt (IPI) to other CPUs
  (Other CPUs invoke SW handler and flush mapping from TLB)
  (Other CPUs ack CPU1)
  Flushes mapping in CPU1
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
Page Table

## Slide 30: TLB shootdown
Thread1 frees memory
  munmap, not just free
OS on CPU1:
  Locks entry in page table
  Sends inter-processor interrupt (IPI) to other CPUs
  (Other CPUs invoke SW handler and flush mapping from TLB)
  (Other CPUs ack CPU1)
  Flushes mapping in CPU1
  Unlocks entry in page table
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
Page Table

## Slide 31: TLB shootdown
Thread1 frees memory
  munmap, not just free
OS on CPU1:
  Locks entry in page table
  Sends inter-processor interrupt (IPI) to other CPUs
  (Other CPUs invoke SW handler and flush mapping from TLB)
  (Other CPUs ack CPU1)
  Flushes mapping in CPU1
  Unlocks entry in page table
  Resumes execution
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
Page Table

## Slide 32: TLB shootdown: The overhead
TLB shootdowns are a real pain
Example overheads from DiDi paper: Can reach over 5us
Apache Web Server
Word Count

## Slide 33: TLB shootdown: The overhead
The real factor is shootdown frequency
Shootdown frequency increases with:
  Core count
  Multiprogramming environments (e.g., cloud)
Example from the DiDi paper
  Based on a model extrapolated from real systems
  Back in 2011 we had fewer cores
  Later validated by others

## Slide 34: TLB shootdown: HW/SW co-designs
Modern processors still don’t offer full TLB coherence
  I don’t really know why
But big vendors introduced some HW support in recent years
  Intel RAR (Remote Action Request)
  AMD INVLPGB

## Slide 35: TLB shootdown: Intel RAR
Introduced in 2021
Avoids interrupting remote cores

## Slide 36: TLB shootdown: Intel RAR
Thread frees memory
  munmap, not just free
OS on CPU1:
  Locks entry in page table
  Sends inter-processor interrupt (IPI) to other CPUs
  (Other CPUs invoke SW handler and flush mapping from TLB)
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1
VA1->PA1
Page Table

## Slide 37: TLB shootdown
Thread frees memory
  munmap, not just free
OS on CPU1:
  Locks entry in page table
  Sends inter-processor interrupt (IPI) to other CPUs
  (Other CPUs invoke SW handler and flush mapping from TLB)
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1
VA1->PA1
Page Table

## Slide 38: TLB shootdown: Intel RAR
Introduced in 2021
Avoids interrupting remote cores
Intel Remote Action Request: White Paper, July 2021

## Slide 39: TLB shootdown: Intel RAR
Introduced in 2021
Avoids interrupting remote cores
Not yet supported in official Linux kernel
  Beta code not stable yet
My take:
  Sounds like interrupt handling takes place in microcode
  Saves the need to invoke handler and save/restore running thread
  Minimal hardware intervention, but also minimal performance gains

## Slide 40: TLB shootdown: AMD INVLPGB
Introduced in late 2002
INVLPGB instruction broadcasts and invalidation request to all cores
  Supports multiple in-flight requests
  TLBSYNC instruction waits for all pending requests

## Slide 41: TLB shootdown
Thread frees memory
  munmap, not just free
OS on CPU1:
  Locks entry in page table
  INVLPGB broadcasts invalidations to all TLBs
  TLBSYNC waits for invalidations to complete
CPU1
TLB
L1
L2
LLC
CPU2
TLB
L1
L2
VA1->PA1
VA1->PA1
Page Table

## Slide 42: TLB shootdown: AMD INVLPGB
Introduced in late 2020
INVLPGB instruction broadcasts and invalidation request to all cores
  Supports multiple in-flight requests
  TLBSYNC instruction waits for all pending requests
Integrated into Linux kernel in March 2025
  Kernel mailing lists reports 2x speedup compared to SW-based shootdown
  My student Gal Dvir measured ~0.5us overhead
My take:
  Seems like a more extensive solution than Intel RAR
  Possibly implemented in microcode(?)

## Slide 43: TLB shootdown: Summary
A real problem in modern CPUs
Identified in academia ~15 years ago
Took industry ~10 years to provide a partial solution
Took another ~5 years to integrate into mainline kernel
Part of a bigger problem:
  Virtual memory (and other HW/SW abstractions) designed in simpler times
  Not a good fit for modern workloads running on manycore CPUs
  We need to rethink these abstractions

## Slide 44: Nested virtual memory translation
Virtual machines are common in cloud environments
We already discussed some of the virtualization overheads
Let’s examine the impact on virtual memory

## Slide 45: Nested virtual memory translation
Each virtual machine “thinks” it is managing its own memory
The guest OS manages page tables for all processes
Guest “thinks” translation is done by computing a sequence of physical addresses:

## Slide 46: Nested virtual memory translation
The host must virtualize the memory translation for the guest
What guest sees as physical, host sees as virtual
  Each “physical” address in the guest is a virtual address in the host
We now have four types of addresses
  gVA (guest virtual address)
  gPA (guest physical address)
  hVA (host virtual address; typically =gPA)
  hPA (host physical address)
Each step of traversing the guest page table requires a gPA -> hPA translation

## Slide 47: Nested page-walk
From 1D page walk to a 2D page-walk

## Slide 48: Nested page-walk
Guest uses gPAs in its page table
Host must translate each gPA to a hPA
Page table base: gPA

## Slide 49: Nested page-walk
Also called 2D address translation
Hypervisor provides a page table for each virtual machine
Hardware performs the double translation:
Overhead: A gVA -> hPA translation may cost 24 memory accesses!

## Slide 50: Nested page-walk: Partial Walk Caches (PwC)
PwCs cache partial translations to shorten the walk
Use address prefixes to get to guest page table entries
9b
9b
9b
9b

## Slide 51: Nested page-walk: Partial Walk Caches (PwC)
PwCs cache partial translations to shorten the walk
Use address prefixes to get to guest page table entries
9b
9b
9b
9b
Index

## Slide 52: Nested page-walk: Partial Walk Caches (PwC)
PwCs cache partial translations to shorten the walk
Use address prefixes to get to guest page table entries
9b
9b
9b
9b
Index

## Slide 53: Nested page-walk: Partial Walk Caches (PwC)
PwCs cache partial translations to shorten the walk
Use address prefixes to get to guest page table entries
9b
9b
9b
9b
Index

## Slide 54: Nested page-walk: Partial Walk Caches (PwC)
PwCs cache partial translations to shorten the walk
Use address prefixes to get to guest page table entries
All PwCs are searched in parallel
  More power, on top of area
9b
9b
9b
9b
Index

## Slide 55: Nested Page Walks: What can we do?
Active research topic
  But no canonical solutions yet
Data centers have to do with what hardware provides…

## Slide 56: Nested page-walk in data centers
Data centers use 1GB pages in hypervisors
Pros:
  shortens walk to 15 mem. Accesses
Cons:
  Moving/swapping 1GB pages takes more time
Page table base: gPA
4KB pages
2MB pages
1GB pages

## Slide 57: Nested page-walk: Overheads
Two seminal papers that introduced the overheads
  Basu et al., “Efficient virtual memory for big memory servers”. In ISCA 2013
  Alam et al., “Do-It-Yourself Virtual Memory Translation”. In ISCA 2017
Very different proposals that target the same problem
Not the only proposals…

## Slide 58: Nested page-walk: Skip translation (Basu’13)
Observation: The overheads of TLB misses is staggering for 4KB and 2MB pages

## Slide 59: Nested page-walk: Skip translation (Basu’13)
Observation: The overheads of TLB misses is staggering for 4KB and 2MB pages
Insight:
  Use some of the physical memory for contiguous memory segments
  Allow direct translation gVA->hPA

## Slide 60: Nested page-walk: Skip translation (Basu’13)
Observation: The overheads of TLB misses is staggering for 4KB and 2MB pages
Insight:
  Use some of the physical memory for contiguous memory segments
  Allow direct translation gVA->hPA
Benefits:

## Slide 61: Nested page-walk: Skip translation (Basu’13)
Pros:
  Observation that memory translation in VMs is a real pain
  Dramatic reduction in translation overheads
Cons:
  Reserving contiguous physical memory impacts hypervisor’s flexibility
  Prone to memory fragmentation

## Slide 62: Nested page-walk: Flexible translation (Alam’17)
Observation 1:
  Translation is a pain even without virtualization
Native execution, 4KB pages (Haswell)

## Slide 63: Nested page-walk: Flexible translation (Alam’17)
Observation 1:
  Translation is a pain even without virtualization
  Gets worse with VMs
4KB pages
2MB pages

## Slide 64: Nested page-walk: Flexible translation (Alam’17)
Observation 1:
  Translation is a pain even without virtualization
  Gets worse with VMs
Observation 2:
  Larger PwCs and L2TLBs help
Translation overhead [%]

## Slide 65: Nested page-walk: Flexible translation (Alam’17)
Observation 1:
  Translation is a pain even without virtualization
  Gets worse with VMs
Observation 2:
  Larger PwCs and L2TLBs help
Insight: The Radix tree data structure is not suitable for all applications

## Slide 66: Nested page-walk: Flexible translation (Alam’17)
Observation 1:
  Translation is a pain even without virtualization
  Gets worse with VMs
Observation 2:
  Larger PwCs and L2TLBs help
Insight: The Radix tree data structure is not suitable for all applications
Proposal:
  Let applications perform memory translation (with some optimizations)
  Permissions are checked when translation is inserted to TLB

## Slide 67: Nested page-walk: Flexible translation (Alam’17)
Benefits (higher is better):

## Slide 68: Nested page-walk: Flexible translation (Alam’17)
Pros:
  Another demonstration that memory translation (not just in VMs) is painful
  Allowing apps to select their own translation data structure is highly beneficial
Cons:
  Not trivial to implement
  Too many changes to existing systems

## Slide 69: Nested page walk: Summary
Virtual memory is an important abstraction, but comes at a cost
Translation consume a large fraction of machine cycles
An active research area with a lot of room for improvement
Part of a bigger problem:
  Virtual memory (and other HW/SW abstractions) designed in simpler times
  Not a good fit for modern workloads running on manycore CPUs
  We need to rethink these abstractions

## Slide 70: Thank you 
Questions?